SCons tool qt4 - Reference
author:
	Philippe Vaucher
author:
	Dirk Baechle
pubdate:
	2010-07-13

This reference lists all the variables that are used within the "qt4" tool, and the available builders. It is intended for SCons tool developers and core programmers, as a normal user you should read the manual instead.
# What it does
The "qt4" tool sets construction variables and registers builders for creating applications and libraries that use the Qt4 framework by Trolltech/Nokia.
It supports the following operations:
## Automatic moc file generation from header files
You do not have to specify moc files explicitly, the tool does it for you. However, there are a few preconditions to do so: Your header file must have the same filebase as your implementation file. It must have one of the suffixes .h, .hpp, .H, .hxx, .hh. You can turn off automatic moc file generation by setting QT4_AUTOSCAN to 0. See also the corresponding builder method Moc4().
## Automatic moc file generation from cxx files
As stated in the Qt documentation, include the moc file at the end of the cxx file. Note that you have to include the file, which is generated by the transformation

${QT4_MOCCXXPREFIX}<basename>${QT4_MOCCXXSUFFIX}
## Handling of .ui files
TODO: describe in a little more detail.
See also the corresponding Uic4 builder method.
## Handling translation files (.ts and .qm)
TODO: describe in a little more detail.
See also the corresponding builder methods Ts4 and Qm4.
## Compiling resource files (.qrc)
TODO: describe in a little more detail.
See also the corresponding Qrc4 builder method.
# Builders

## Moc4
Builds an output file from a moc input file. Moc input files are either header files or cxx files. This builder is only available after using the tool 'qt4'.
Example:

env.Moc4('foo.cpp') # generates foo.moc

## XMoc4
Just like the Moc4 builder, it builds an output file from a moc input file. Moc input files are either header files or cxx files. This builder is only available after using the tool 'qt4'. It is defined separately for the include driven Automoc strategy (#1) and can be controlled via the QT4_XMOC* variables.
Example:

env.XMoc4('foo.h') # generates moc_foo.cpp
env.XMoc4('foo.cpp') # generates foo.moc

## ExplicitMoc4
Just like the Moc4 builder, it builds an output file from a moc input file. However, it does not use any default prefix or suffix for the filenames. You can, and have to, specify the full source and target names explicitly. This builder is only available after using the tool 'qt4'. It can be your last resort, when you have to moc single files from/to exotic filenames.
Example:

env.ExplicitMoc4('moced_foo.cxx','foo.h') # generates moced_foo.cxx

## Uic4
Builds a header file from an .ui file, where the former contains the setup code for a GUI class. This builder is only available after using the tool 'qt4'. Using this builder lets you override the standard naming conventions (be careful: prefixes are always prepended to names of built files; if you don't want prefixes, you may set them to ``).
Example:

env.Uic4('foo.ui') # -> 'ui_foo.h'

## ExplicitUic4
Just like the Uic4 builder, it builds a header file from a .ui input file. However, it does not use any default prefix or suffix for the filenames. You can, and have to, specify the full source and target names explicitly. This builder is only available after using the tool 'qt4'. It can be your last resort, when you have to convert .ui files to exotic filenames.
Example:

env.ExplicitUic4('uiced_foo.hpp','foo.ui') # generates uiced_foo.hpp

## Qrc4
Builds a cxx file, containing all resources from the given .qrc file. This builder is only available after using the tool 'qt4'.
Example:

env.Qrc4('foo.qrc') # -> ['qrc_foo.cc']

## Ts4
Scans the source files in the given path for tr() marked strings, that should get translated. Writes a .ts file for the Qt Linguist. This builder is only available after using the tool 'qt4'.
Example:

env.Ts4('foo.ts','.') # -> ['foo.ts']

## Qm4
Compiles a given .ts file (Qt Linguist) into a binary .qm file. This builder is only available after using the tool 'qt4'.
Example:

env.Qm4('foo.ts') # -> ['foo.qm']

# Variables